## Slide 1
The First Assignment
Hangyu Shao, Run Zhu
Architecture of Computer Networks

## Slide 2
CONTENTS
Problem Definition
01
Answers and Details
02
Reference
03

## Slide 3
PART
ONE
Problem Definition

## Slide 4
Task One
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 5
Task Two
List the available residential access technologies in your city. For each type of access, provide the advertised downstream rate, upstream rate, and monthly price.
Describe the most popular wireless Internet access technologies today. Compare and contrast them.
Why will two ISPs at the same level of the hierarchy often peer with each other? How does an IXP earn money?
Some content providers have created their own networks. Describe Google’s network. What motivates content providers to create these networks?

## Slide 6
PART
TWO
Approaches and
Details

## Slide 7
Task One
Transform the problem into:
Choose 11 in 35 users:
(2) 11 users “active” time:
(3) Probability of choose 11 in 35 users and “active”:
Probability Problem

## Slide 8
Task Two - Wireless Internet Access Technologies
A: It can be mainly divided into two kinds.
Wireless LAN
In a wireless LAN, wireless users transmit/receive packets to/from a base station (wireless access point) within a radius of few tens of meters. The base station is typically connected to the wired Internet and thus serves to connect wireless users to the wired network.
2. Wide-area wireless access network
In these systems, packets are transmitted over the same wireless infrastructure used for cellular telephony, with the base station thus being managed by a telecommunications provider. This provides wireless access to users within a radius of tens of kilometers of the base station.
There are many detailed Wireless Internet Access Technologies.
Q: Describe the most popular wireless Internet access technologies today. Compare and contrast them.

## Slide 9
Task Two - Wireless Internet Access Technologies
Cellular Digital Packet Data (CDPD)
General Packet Radio Service (GPRS)
Enhanced Data Rate for GSM Evolution (EDGE)
Code Division Multiple Access (CDMA)
Satellite Internet Access System (SIAS)
Wireless Local Access Network (WLAN)
Wide-area Wireless Access Network (WWAN)
Wireless Application Protocol (WAP)
Bluetooth
9

## Slide 10
Task Two - Wireless Internet Access Technologies
Cellular Digital Packet Data (CDPD)
General Packet Radio Service (GPRS)
Enhanced Data Rate for GSM Evolution (EDGE)
CDPD is a mobile service technology specially used in data network. It uses packet switching technology instead of circuit switching technology.
GPRS breaks through the thinking that GSM network can only provide circuit switching, and introduces packet switching mode into GSM network.
EDGE adopts TDMA technology, and its frame structure is the same as that of GSM.
10

## Slide 11
Task Two - Wireless Internet Access Technologies
Broadband Code Division Multiple Access (BCDMA)
Satellite Internet Access System (SIAS)
Wireless Local Access Network (WLAN)
Broadband CDMA meets the high data rate requirement of wireless Internet access by optimizing high-speed packet data transmission in broadband.
The main advantage of Internet satellite access is that it can provide users with more bandwidth, improve access speed, and solve the problem of low speed of browsing Web sites and downloading files.
WLAN refers to the application of wireless communication technology to interconnect computer equipment to form a network system that can communicate with each other and realize resource sharing.
11

## Slide 12
Task Two - Wireless Internet Access Technologies
Wide-area Wireless Access Network (WWAN)
Wireless Application Protocol (WAP)
Bluetooth
WWAN is a communication mode that uses wireless network to connect local area network (LAN) with extremely dispersed physical distance.
WAP is a kind of communication protocol. Its proposal and development are based on the need of accessing the Internet in mobile.
Bluetooth technology aims to cancel wired connection and realize wireless interconnection between digital devices to ensure that most common computers and communication devices can communicate conveniently.

## Slide 13
Task Two - Wireless Internet Access Technologies
Name | Cellular Digital Packet Data (CDPD) | General Packet Radio Service (GPRS) | Enhanced Data Rate for GSM Evolution (EDGE) | Code Division Multiple Access (CDMA) | Satellite Internet Access System (SIAS) | Wireless Local Access Network (WLAN) | Wireless Application Protocol (WAP) | Bluetooth | Wide-area Wireless Access Network (WWAN)
Time | 1995 | 1999 | 2003 | 1995 | / | 1997 | 1998 | 1998 | 2002
Theoretical Speed | 5～10Kbit/s | 50～100Kbit/s | 100～300Kbit/s | 50～200Kbit/s | ～4Mbit/s | ～300Mbit/s | ～300Kbit/s | ～24Mbit/s | ～3Mbit/s
Features | uses packet switching technology | introduces packet switching mode into GSM network | frame structure is the same as that of GSM | optimizing high-speed packet data transmission in broadband | solve the problem of low speed of browsing Web sites | transmission between network and terminal links | based on the need of accessing the Internet in mobile | cancel wired connection and realize wireless interconnection | communication mode that uses wireless network

## Slide 14
Other Tasks - Residential Access Technologies
A:
1. Dial-up modem over telephone line
Downstream rate:8Mbps Upstream rate:640Kpbs
Monthly price: almost 4.2yuan/h, 250yuan/month
2. DSL over telephone line
Downstream rate: 1.5MB/s Upstream rate: 640KB/s
Monthly price: almost 30yuan/month
3. Cable to HFC
Downstream rate:30Mbps Upstream rate:2.56Mbps
Monthly price: almost 20yuan/month
Q: List the available residential access technologies in your city. For each type of access, provide the advertised downstream rate, upstream rate, and monthly price.

## Slide 15
Other Tasks - ISPs
A:
If the two ISPs do not peer with each other, then when they send traffic to each other they have to send the traffic through a provider ISP (intermediary), to which they have to pay for carrying the traffic. By peering with each other directly, the two ISPs can reduce their payments to their provider ISPs.
An Internet Exchange Points (IXP) is a meeting point where multiple ISPs can connect and/or peer together. An ISP earns its money by charging each of the ISPs that connect to the IXP a relatively small fee, which may depend on the amount of traffic sent to or received from the IXP.
Q: Why will two ISPs at the same level of the hierarchy often peer with each other? How does an IXP earn money?

## Slide 16
Other Tasks - Google’s Network
A:
Description:
Google's private network connects together all its data centers, big and small. Traffic between the Google data centers passes over its private network rather than over the public Internet. Many of these data centers are located in, or close to, lower tier ISPs. Therefore, when Google delivers content to a user, it often can bypass higher tier ISPs.
Motivation:
First, the content provider has more control over the user experience, since it has to use few intermediary ISPs.
Second, it can save money by sending less traffic into provider networks.
Third, if ISPs decide to charge more money to highly profitable content providers, the content providers can avoid these extra payments.
Q: Some content providers have created their own networks. Describe Google’s network. What motivates content providers to create these networks?

## Slide 17
PART
Three
Reference

## Slide 18
Reference
[1] 陈晓范,吴昊. 家庭宽带无线接入技术探究[J]. 时代教育,2013,(23):169-170.doi:10.3969/j.issn.1672-8181.2013.23.125.
[2] 万选 . 无线宽带接入技术在电信网络演进中的定位思考 [J]. 河南科技 ,2014,(10):4-5.
[3] A Survey of Downlink Non-Orthogonal Multiple Access for 5G Wireless Communication Networks[J]. WEI Zhiqiang,YUAN Jinhong,Derrick Wing Kwan Ng,Maged Elkashlan,DING Zhiguo. ZTE Communications. 2016(04)
[4] On Limits of Wireless Communications in a Fading Environment when Using Multiple Antennas[J] . G.J. Foschini,M.J. Gans. Wireless Personal Communications . 1998 (3)
[5] Living on the edge:The role of proactive caching in 5G wireless networks. Bastug E,Bennis M,Debbah M. IEEE Communications Magazine . 2014

## Slide 19
THANKS